## Slide 1: Intelligent Manufacturing System Layout Design
Muhammad Ridwan Andi Purnomo, ST, MSc, PhD
Department of Industrial Engineering
Faculty of Industrial Technology
Universitas Islam Indonesia
2012

## Slide 2: Layout Type
Layout of manufacturing system is defined based on the requirement.
  MTS  mass production  flowshop (high productivity, low flexibility)
  MTO  order driven production  jobshop (high flexibility, low productivity)
  Repetitive jobshop  needs middle flexibility and productivity.
Combination of flowshop and jobshop  group technology.

## Slide 3: Group Technology (GT)
Manufacturing system is grouped to be several manufacturing cell.
All parts with similar process is grouped to be processed in a manufacturing cell.
In a manufacturing cell idle machines must be avoided.
Intercellular part must be avoided.

## Slide 4: Manufacturing Cell Forming
Input data: incident matrix  based on OPC.
Example:

## Slide 5: Conventional Method
Similarity coefficient
Rank Order Clustering (ROC)
Etc.

## Slide 6: Intelligent Optimisation
Very complicated problem needs very hard mathematical model as well.
Very hard mathematical model needs analytical software to solve.
Analytical software needs very high computer spec and most of analytical software has limited capability.
When model is over complicated, analytical software applies an approximation algorithm to solve  no optimum solution warranty.
Genetic Algorithm can be used as optimisation technique.

## Slide 7: Genetic Algorithm (GA)
Introduced by John Holland (1970).
The aim was to make computers do what nature does.
Nature has an ability to adapt and learn without being told what to do.
In other words, nature finds good chromosomes blindly, and GA do the same.
GA can be represented by a sequence of procedural steps for moving from one population of artificial ‘chromosomes’ to a new population.
It uses ‘natural’ selection and genetics-inspired techniques known as crossover and mutation.

## Slide 8: Genetic Algorithm (GA)
Solution to be found has to be encoded in the form of a chromosome.
The fitness of a chromosome will be evaluated using fitness function.
The critical things in GA are ‘how to encode a solution to be a chromosome in effective way’ and ‘how to define fitness function for a chromosome’.
Fitness function  related with objective function of the real case.

## Slide 9: Example of Chromosome and fitness function
In a case to maximise function z = 3x1 – 5x2
  Chromosome (binary):
  Fitness: z
  In a case of travelling salesman problem (TSP) with 9 cities
    Chromosome (permutation or combinatorial):
    Fitness: 1/ total distance or B – total distance, B is very big number

## Slide 10: Cycle of GA

## Slide 11: GA for GT
Decision: group of parts and machines.
Objective: minimise number of delayed machines inside a cell and minimise intercellular parts.

## Slide 12: Spreadsheet Modelling
Much more simple then mathematical modelling.
Easy to understand.
There are so many mathematical built in function that can be used.
Able to communicate with another software.

## Slide 13: Thank You !