## Slide 1: Scheduling in Flexible Machine
Muhammad Ridwan Andi Purnomo, ST, MSc, PhD
Department of Industrial Engineering
Faculty of Industrial Technology
Universitas Islam Indonesia
2013

## Slide 2: Introduction
In Flexible Manufacturing System, one of the characteristic is the use of flexible machine  can be used to process several material with particular specification.
Common problem in flexible machine scheduling is the management of resources to process several parts.
One of the flexible machine is flexible forging machine.

## Slide 3: Factors to be considered
Part needs specific jig and fixture  set up time for loading and unloading.
Changeover of the tools to process all of the parts to be processed.
If several parts to be processed, then:
  Loading and unloading time must be considered.
  Changeover of the tools affect processing time.
  Sequence of the parts affect the total processing time.

## Slide 4: Flexible Forging Machine Scheduling
It is single machine scheduling.
Input data is the matrix of tools and jig and fixture changeover to process all of the parts.
It can be seen as Travelling Salesman Problem (TSP).
In TSP, solution to be found is the sequence of the city to be visited, in FFM scheduling the solution to be found is the sequence of the part to be processed.

## Slide 5: Greedy algorithm to solve FFM Scheduling
The concept is selecting next part with minimum changeover time and does not care whether this will lead to a wrong result or not.
The algorithm:
Step 1: Select a part randomly as the starting part.
Step 2: Select other part with minimum changeover time.
Step 3: Update the starting part with the selected part.
Step 4: Repeat step 2 until all of the parts are scheduled.

## Slide 6: Example of FFM scheduling with Greedy Algorithm
Six parts to be processed in FFM with changeover time of each part as shown as follow:
If we start from part 1 (randomly selected), then the result is:
1-3-5-6-4-2.

## Slide 7: FFM with more than one tools required
Sometime, each part needs more than one tool in processing.
Part-tool matrix is required.
Hamming distance formula is required to identify changeover time from a part to each other.

## Slide 8: Example of FFM scheduling with more than one tools required
Consider part-tool matrix bellow:

## Slide 9: Example of FFM scheduling with more than one tools required
Hamming distance matrix can be determined as follow:
Applying greedy algorithm, the result is: 2-5-3-1-4.

## Slide 10: To be considered
Greedy algorithm is started from random point, how to initialise it in order to get better result?
Greedy algorithm considers just one step ahead to minimise the distance. By considering two steps ahead, it might better.
In large scale problem, the use of Genetic Algorithm can produce optimum or near optimum result.

## Slide 11: Thank You !