## Slide 1
Attribute Control Chart

## Slide 2
Introduction
Control Chart For Attribute
The term attribute, as used in quality control, refers to quality characteristics that “conform to specifications” Or “do not conform to specifications”

## Slide 3
Measurement can be made but are not made because time, cost or need.
There are two (2) types atribute :
Measurements are not possible – for example, visually inspected items such as color, missing parts, scratches and damage

## Slide 4
Percent Defective Chart = p – chart
If the item recorded is the fraction of unacceptable parts made in a larger batch of parts, the appropriate control chart is the percent defective chart. The centreline is at p, the mean proportion defective.

## Slide 5
Example:
Jersey Glass Company, Inc. produces small hand mirrors. Jersey Glass runs a day and evening shift each weekday. The quality assurance department (QA) monitors the quality of the mirrors twice during the day shift and twice during the evening shift. QA selects and carefully inspect a random sample of 50 mirrors once every 4 hours. Each mirror is classified as either acceptable or unacceptable. Finally QA counts the number of mirrors in the sample that do not conform to quality specifications. Listed below are the results of these checks over the last 10 business days.

## Slide 7
Construct a percent defective chart for this process. What are the upper and lower control limits? Interpret the results Does it appear the process is out of control during the period?
The first step is to determine the mean proportion defective. We use formula (1).
So we estimate that 0.098 of the mirrors produced during the period do not meet specifications.

## Slide 8
Date | Number Sampled | Defects | Fraction Defect | Date | Number Sampled | Defects | Fraction Defect
10-Oct | 50 | 1 | 0.02 | 17-Oct | 50 | 7 | 0.14
 | 50 | 0 | 0.00 |  | 50 | 9 | 0.18
 | 50 | 9 | 0.18 |  | 50 | 0 | 0.00
 | 50 | 9 | 0.18 |  | 50 | 8 | 0.16
11-Oct | 50 | 4 | 0.08 | 18-Oct | 50 | 6 | 0.12
 | 50 | 4 | 0.08 |  | 50 | 9 | 0.18
 | 50 | 5 | 0.10 |  | 50 | 6 | 0.12
 | 50 | 3 | 0.06 |  | 50 | 1 | 0.02
12-Oct | 50 | 9 | 0.18 | 19-Oct | 50 | 4 | 0.08
 | 50 | 3 | 0.06 |  | 50 | 5 | 0.10
 | 50 | 10 | 0.20 |  | 50 | 2 | 0.04
 | 50 | 2 | 0.04 |  | 50 | 5 | 0.10
13-Oct | 50 | 2 | 0.04 | 20-Oct | 50 | 0 | 0.00
 | 50 | 4 | 0.08 |  | 50 | 0 | 0.00
 | 50 | 9 | 0.18 |  | 50 | 4 | 0.08
 | 50 | 4 | 0.08 |  | 50 | 7 | 0.14
14-Oct | 50 | 6 | 0.12 | 21-Oct | 50 | 5 | 0.10
 | 50 | 9 | 0.18 |  | 50 | 1 | 0.02
 | 50 | 2 | 0.04 |  | 50 | 9 | 0.18
 | 50 | 4 | 0.08 |  | 50 | 9 | 0.18
 |  |  |  | Total | 2000 | 196 | 
Reference: Lind/Marchal/ Wathan. 2010. Statistical Technique in Business and Economics, 14th edition

## Slide 9
The upper and lower control limits are computed by using formula (3)
From the above calculations, the upper control limits is 0.2241, found by 0.098+ 0.1261. The lower control limits is 0. Why? The lower control limits by the formula is 0.098 – 0.1261 = - 0.0281. However, a negative proportion defective is not possible, so the smallest value is 0. We set the control limits at 0 and 0.2241. Any sample outside theses limits indicates the quality level of the process has changed.

## Slide 10
c- Bar Charts
The c-bar chart plots the number of defects or failure per unit.
Example
The publisher of the Oak Harbor Daily Telegraph is concerned about the number of misspelled words in the daily newspaper. It does not print a paper on Saturday or Sunday. In an effort to control the problem and promote the need for correct spelling, a control chart will be used. The number of misspelled words found in the final edition of the paper for the last 10 days is: 5, 6, 3, 0, 4, 5, 1, 2, 7 and 4. Determine the appropriate control limits and interpret the chart. Where there any days during the period that the number of misspelled words was out of control?

## Slide 11
Solution:
During the 10-day period there were a total of 37 misspelled words. The mean number of misspelled words per edition is 3.7. The number of misspelled words per edition follows the Poisson probability distribution. The standard deviation is the square root of the mean:
To find the upper control limit we use formula (4). The lower control limit is zero.
The computed lower control limit would be 3.7 – 3(1.924) = -2.07.

## Slide 12
U dalam U-chart berarti “unit” cacat dalam kelompok sampel. U-chart menghitung titik cacat per unit laporan pemeriksaan dalam periode yang mungkin memiliki ukuran sampel bervariasi (banyak item yang diperiksa). Jika C-chart menghitung titik cacat dalam satu item yang sama, maka U-chart digunakan dalam kasus di mana sampel yang diambil bervariasi atau memang seluruh produk yang dihasilkan akan diuji. Hal ini berarti bahwa U-chart digunakan jika ukuran sampel lebih dari satu unit atau mungkin bervariasi dari waktu ke waktu. Jika pada C-chart, kita langsung mem-plot-kan data cacat langsung ke dalam peta kendali; maka pada U-chart, kita perlu menghitung terlebih dahulu u cacat untuk setiap n sampel, yaitu:
Nilai ui inilah yang akan di-plot-kan dalam peta kendali, yang mana xi adalah jumlah cacat dalam subgrup ke-i dan ni adalah jumlah unit laporan pemeriksaan dalam subgrup ke-i.

## Slide 13
Pada sebuah lini finishing industri tekstil, inpektur QC memeriksa cacat celupan kain setiap 50 meter persegi, yang mana luas kain per roll bervariasi. Data 10 roll kain ditunjukan Tabel di bawah ini.
Tabel Data kejadian cacat dalam celupan kain dan batas-batas kendali untuk U-chart
http://eriskusnadi.wordpress.com/2012/06/09/statistical-process-control/8/

## Slide 14
u | = | 153
 |  | 107,5
Garis pusat U-chart adalah rata-rata jumlah cacat per unit pemeriksaan, yaitu rata-rata jumlah cacat per 50 meter persegi, dihitung sebagai berikut: (Perhatikan bahwa u adalah rasio dari jumlah cacat teramati dengan jumlah total unit pemeriksaan)
Batas-batas kendali pada Tabel 7 dihitung dengan model harian/individu. Lebar batas-batas kendali bervariasi mengikuti ni, jumlah unit pemeriksaan dalam roll kain. Perhitungan batas-batas kendali ditampilkan dua kolom terakhir Tabel 7, dan plot U-chart ditunjukkan Gambar 8 dibawah ini.

## Slide 15
Jika P-chart memonitor proporsi cacat (p̂) dalam jumlah sampel (n), maka NP-chart memonitor jumlah cacat itu sendiri. N dalam NP-chart berarti “number” atau “jumlah”, yaitu jumlah unit-unit yang tidak sesuai (nonconforming units) dalam sebuah sampel. NP-chart hanya menggunakan pengukuran sampel konstan. Montgomery (2005) mengatakan:
Many non-statistically trained personnel find the np chart easier to interpret than the usual fraction nonconforming control chart. (p. 279).
Pada umumnya data jumlah item cacat memang lebih disukai dan mudah untuk diinteprestasikan dalam pembuatan laporan dibandingkan dengan data proporsi.
Berikut perbedaan NP-chart dan P-chart:
Batas kendali dihitung dengan np ± 3√ np(1 – p) , yang mana n adalah ukuran sampel dan p adalah proporsi cacat. Jika nilai standar untuk p tidak tersedia, (rata-rata p) dapat digunakan untuk menghampiri p.
Data yang di-plot-kan pada peta kendali adalah jumlah cacat (np), bukan proporsi cacat (p̂).
Ukuran sampel (n) harus konstan.

## Slide 16
Sebagai contoh perhatikan Tabel di bawah ini.
Tabel Data untuk NP-chart, ukuran sampel n = 50

## Slide 17
Dari 30 sampel pada Tabel 5 di atas terdapat ∑i=1,…,30 Di = 347 unit cacat, dan nilai p dihampiri dengan
Dengan n = 50, parameter untuk NP-chart adalah sebagai berikut: