## Slide 1: Engineering Anthropometry
Anthropometry is the branch of the human sciences that deals with human body measurements: particularly with measurement of body size, shape, strength and working capacity.
Anthropometrics measurements are a critical element in equipment and workplace/workspace design
Utilization of anthropometrics data will enable designers to accommodate a desired portion of potential user population in their designs.
In anthropometrics data, it is important to understand the population (a group of people) being described.

## Slide 2: The basic application of anthropometrics data in design
There are two types of dimensions that determine what the design dimensions should be taken:
1.Clearance dimensions determine the minimum space required for a human being to perform work activities in the workplace, such as operating and maintaining machines and so on.
Clearances are established by the larger people from the expected user population (e.g., the size of a door frame is determined by the size of the largest expected user)
2. Reach dimensions determine the maximum space allowable for the human being who operates equipment and are established by the smaller people in the expected user population (e.g., control height is determined by accommodating shorter people)

## Slide 3: Basic ergonomic design philosophies
There are three basic design philosophies utilized by ergonomists as applying anthropometrics data:
1. Design for the average. The problem of designing for the average is that the design may end up fitting no one, because no one is average in dimensions. However, the design for the average philosophy is utilized for designs involving public facilities.
2. Design for the extremes. The problem of designing for the extremes is the cost associated with such a design philosophy. Assuming that an automobile seat is designed to accommodate the smallest person, would it be feasible for the largest person to use the vehicle?
3. Design for the range. The most common design philosophy of the ergonomist is to design for a range of the population. A typical range of the 5th to 95th percentile of the population is used. Such a design would be expected to accommodate 90% of the design population. Design ranges can be wider or narrower and are typically determined by task criticality and cost.

## Slide 4: Statistical basis of anthropometry
Assume that the random variable X represents a specific anthropometrics measure (e.g. seating height) of a certain population. Assume also that xp is the pth percentile of X. Then it defines:
P(X  xp) = p
as the proportion of the population whose seating height are equal to or less than xp. That is, “100*p” percent of that population are of seating height equal to or less than xp.
It is usually assumed that human anthropometrics characteristics are normally distributed. That is, we can state that the anthropometrics variable X has a normal distribution with mean  and standard deviation . Then Z = (X - )/ has a standard normal distribution and we can rewrite equation as:
P(X  xp) = P[(X- )/  (xp-x)/s] = p or P(Z  zp) = p

## Slide 5: Statistical basis of anthropometry
where zp = (xp-x)/s values are given in standard normal probability (often called the Z-dsitribution) table for value of p (note that the size of the sample for which x is calculated should be n  30; otherwise, tp and t-distribution table must be used instead of zp). We can use zp = (xp-x)/s to write the following equation:
xp = x ± zp  s
where :
x = sample mean
s = sample standard deviation
xp = pth percentile value of the variable X
zp = standard normal value corresponding to pth percentile value of X

## Slide 6: Anthropometrics data
There are two types of anthropometrics data measurements:
1. Structural (static) measurements
These measurements are concerned with the dimensions of the body segments at stationary positions (not in motion). They include the body’s contour dimensions (e.g., stature, sitting height, length of upper arm, hip breadth) and skeletal dimension (e.g., the distance between the centers of joints, such as between the hip and the knee)
2. Functional (dynamic) measurements
These measurements are concerned with the dimensions of the body segments during physical activities. Examples are reach envelopes, crawling length and height, kneeling height, and range of angular movement of joints

## Slide 7: Body segments
Determination of the center of mass (or center of gravity) and weight distribution of the human body and its segments is needed in human biomechanical assessment
Such data, along with understanding basic mechanics, are useful in:
1. Design of equipment operated by humans in various postures
2. Design of workstation (e.g., seats for industrial workers, vehicle operators and aircraft pilots)
3. Biomechanical applications
The location of the centers of mass (c.m) of body segments as a percentage of the length of their corresponding body segments are graphically shown in Figure 4.3.
Since the mass of each individual body segment increases with the total body mass increase, the mass of each segment can be expressed in term of a percentage of total body mass (Winter, 1990). See Table 4.4 and Figure 4.4.

## Slide 8: Use of anthropometrics data in design
The procedure for the use anthropometrics data is as follow:
1. Define the equipment’s potential user population (e.g., worldwide population, US civilian)
2. Choose the proportion of the population to be accommodated by the design (I.e., 90% and 95% are most common)
3. Determine the body dimensions important in design (I.e., seating eye height, knuckle height,etc). Then, in turn, determine the type of accommodation, whether it is a reach or clearance situation
4. Determine the percentile value of the dimension (determined in step 3) for the chosen proportion of the population (determined in step 2) from anthropometrics table. Where the percentile values are not readily provided, use the mean and standard deviation of the dimension from anthropometrics data
5. Determine the relevant allowances such as type of clothing and personal equipment worn by the users, gloves, etc.