## Slide 2: Human – Machine System
Perceives the status of the machine through Displays
Interprets and mentally process the perceived information
Makes a decision
Conveys the decision to the machine through manually operated Controls
Poor ergonomics designs lead to waste of time and money, and often tragedies

## Slide 3: Ergonomics of Human-Machine System
The design of tools to match the physical characteristics of the worker with the functioning of the tools
The design of the workplace and work space to meet the physical characteristics of the worker
The design of controls and displays to allow the worker to operate and monitor the work system process efficiently with minimum errors
The development of job procedures that meet the worker’s capabilities
The minimization of the effects of external factors (i.e. thermal condition, illumination, noise, and vibration) on the worker in the workplaces

## Slide 4: Steps in System Designs
Objectives determination
  The desired output
  What the system should accomplish
  Characteristic of output and tolerance or error level
Input specification
  The required input to obtain the output
  The required materials, work skills, and resources constraints
Process description
  The process must be described
  The required function and task as well as the constraint
Functional allocation
  The identified function are allocated to the human operators or machines
Interface design
  The interface between the human operator and other system component are so designed to optimize human performance and minimize risks of human errors and injuries
    Workstation
    Controls are designed based on worker capabilities and limitation
    Displays should be user-friendly for the worker to understand them easily, so that the risk of errors is minimized
Facilitator design
  All materials and procedures should be designed for the intended users
Testing and evaluation of the system

## Slide 5: Display
A variety of display are to interact with the human sensory systems:
  Visual displays
    Digital
    Analog
  Auditory displays
  Tactile, olfactory, and taste display (not common)
There are three common types of visual display instruments found in industry:
  A window with digital read-out (counters)
  A (fixed) circular scale with moving pointer
  A fixed pointer over a moving scale

## Slide 6
Counter
Fixed scale with moving pointer
Fixed pointer with moving scale

## Slide 7: Guidelines for Designing Display
A display should present the minimum amount of information necessary for the worker to make a decision based on the information displayed
Use digital read-out displays when quick and accurate readings are to be made
Use circular or semicircular scales instead of vertical or horizontal scale display where possible and if space permits
Increment scale numbering in a clockwise direction on circular/semicircular scale, upward on a vertical, and to the right on a horizontal scale
Use a display with a moving pointer on a fixed, circular scale if it is necessary to monitor how a process is changing, or to note the amplitude of change
Avoid the use of displays with moving scales and fixed pointers since it is not easy to memorize the previous reading, nor to assess the extent of movement

## Slide 8: Guidelines for Designing Display
The major scale markers should be numbered in a natural and easily recognizable fashion
Avoid multi scale, multiple-pointer, and non linier scale displays, whenever possible
Install displays in the direct line of sight of the operator and avoid any obstructions
Avoid glare in the displays
Avoid small size or illegible displays
Use capital letters for single word or short identification sentences since they are readable at a greater distance than lower case letters
The display must be readable from the operator’s normal location
The size of letters and figures, thickness of lines and their distance apart must be determined based on the viewing distance between the eye and the display (see table and figure)

## Slide 9
Recommended minimum letter and numeral height |  | 
Nature of markings | Low lighting | Adequate lighting
Critical markings, position variable (digital read-outs or moving scales) Critical markings, position fixed (emergency instruction, numbers on fixed scales, and control and switch markings) Non-critical markings (identification labels, instructions, non-emergency labels) | 0.20 in (5 mm) 0.15 in (3.75 mm) 0.05 in (1.25 mm) | 0.12 in (3 mm) 0.10 in (2.5 mm) 0.05 in (1.25 mm)
Notes
The values are given for a 28 in (71 cm) viewing distance. The values will increase or decrease in proportion to the increase or decrease in the viewing distance
Luminance (brightness) up to 1 fL or 3.4 cd.m-2 is considered as low lighting
Adapted from Grether and Baker (1972)

## Slide 10
The heights and widths of major, immediate, and minor graduation marks should not be less than the values given in figure below

## Slide 11: Guidelines for Designing Display
Under normal illumination, graduation marks may be spaced as close as 0.9 mm (0.035 in), but the space should never be less than twice the stroke-width for white marks on black dial faces.
Label displays clearly to prevent confusion
Signs and labels should contrast with their background and be of proper size and color
Icons and symbolic signs are very quick in conveying information to the human operator.
Provide adequate illumination and prevent shadows on the display surfaces

## Slide 12: Guidelines for Designing Warning Lights
Size
  Warning lights should subtend at least 1° of visual angle
Color
  Colors in the order of eliciting fast human responses are first, red; second, green; third, yellow; and fourth, white.
  Since red normally indicates danger to most people, warning lights should generally be red
Flash rate
  A flash light is more effective than a steady light in attracting someone’s attention.
  An optimum flash light is 4 times per second. It can be in the range of 3 – 10 times per second
Contrast with background
  Warning light should be bright enough to get attention
  The light should be at least twice as bright as its immediate background
  Warning light should also contrast with background
Multimedia presentation
  An auditory signal can be used for getting extra attention or as a back up system for the visual warning signal.
  Auditory signals are also effective for operators who move around the workplace and may be out of the visual field of a warning light
Notes: <number>

## Slide 13: Control
Controls = activators
  Transmit inputs to a piece of equipment
Use f Controls:
  Activate or shutdown equipment
  Make a discrete setting, such as making a separate or distinct adjustment like selecting a TV Channel
  Make a quantitative setting such as selecting a temperature on thermostat
  Apply continuous control, such as steering an automobile
  Enter data

## Slide 14: Controls
On the basis of the action required, controls are of following two types:
  Discrete-action controls
    This control can be set to any exact position from a limited number of position
    This type of controls are suitable for turning equipment on or off, changing modes of operation, and selecting meter scale
    This controls includes toggle switches, push button, thumbwheels, legend switches, and rotary selector switches
  Continuous-action controls
    Continuous-action control can be set at any position within the range of its movement
    This type of control is used for opening or closing valves, adjusting displays, and varying potentiometers.
    Ex.: hand wheels, knob, hand cranks, levers, joystick, and pedals
Based on the amount muscular effort required, manual controls are classified into the following two categories:
  Nimble (light) controls, which require little muscular effort
  Heavy controls, which require muscular effort

## Slide 15: Guidelines for Designing and Selecting Controls
Controls should be designed based on anatomy and functional characteristics of body limbs
The force, speed, accuracy, or range of movement required by control should not exceed the capabilities of the least capable operator.
Type of control can be easily operated with fingers (use push buttons, tumbler switches, and rotating knobs for operation requiring little movement or muscular effort)
Use long-armed lavers, cranks, hand-wheels, and pedals for operation requiring muscular effort over a long distance, and requiring little precision
The number of controls should be minimized, and their movements should be simple, natural, and easy to perform.

## Slide 16: Guidelines for Designing and Selecting Controls
Control movements should be as short as possible, consistent with the requirements of accuracy and feel
Control should show a positive sign of activation so that malfunction can be immediately apparent to the operator
Control action should result in a positive indication to the operator that there has been a system response
Control should be resistant to abuse and temper
Control surfaces should be designed to prevent the accidental activation of the control by a slipping finger, hand, or foot
Controls should have sufficient resistance so that their inadvertent activation by the weight of a hand or foot is prevented

## Slide 17: Guidelines for Installation and Layout of Controls
Install controls near the operator
Install hand operated controls so that they can easily be reached and grasped
Install heavy levers, that requires the use of a large muscle group of the arm, at slightly below shoulder height for standing and at elbow for sitting
Install controls at either side of the center of the operator’s position rather than mounting them in the center
Install cranks that require a high level of torque so that the turning handle is parallel to the frontal plane of the body
Install controls in full view of the user
The distance between neighboring controls must be sufficient to avoid accidental activation
Install foot controls in such a way that accidental activation, which may lead to potential hazards and undesirable consequences , can be avoided
Consider the human anatomy in specifying distance between controls
Use a appropriate methods of control coding to enable the operator to identify each control correctly and quickly.

## Slide 18: Guidelines for Control-Display Compatibility
The direction of movement of control should be compatible with the direction of movement of displays.
The moving scale with a fixed indicator should move to the left (counterclockwise) when the control is moved to the right (clockwise),
The scale values should increase from left to right (clockwise), so that the rotation of the scale to the left shows increased readings
When a hand lever is moved upwards, forwards, or to the right, the display reading should increase or switch should move to the on position
Controls should be installed near to the displays which they affect
The control should be installed either below the display

## Slide 19: Guidelines for Control-Display Compatibility
The type, location, and orientation of the control should be compatible with the system response through the display
Identification labels should be placed above the controls and identical above the corresponding display instrument
If the controls have to be in one panel and the displays in another, the two sets should be laid out in the same order and arrangement.
If a series of controls are normally operated in sequence, they and their corresponding display instruments should be arranged on the panel in the same order. From left to right
When arranging a group of controls and displays, the controls and displays that are used more often should be located directly in front of the operator, and others to the sides.

## Slide 23: Control Design